## Slide 1: Introduction to Microprocessor
Md. Shafqat Talukder Rakin
Lecturer, Department of CSE,
United International University
Email id : shafqat@cse.uiu.ac.bd
Courtesy: Nasif M. Sir

## Slide 2: Overview of microcomputer
2
structure and operation

## Slide 3
3

## Slide 4: What are we going to learn
4
Microprocessor and Interfacing
Microcomputer
8086 microprocessor
Interfacing
Microcontroller
ATMEGA32
Serial Protocols

## Slide 5: Major Parts Of a Microcomputer
5
CPU
Memory
Input / Output circuitry
Buses:
  Address bus
  Data bus
  Control bus

## Slide 6: Micro-computer overview
6

## Slide 7
7

## Slide 8
8

## Slide 9: Central Processing Unit (CPU)
It controls the operation of computer
The CPU fetches binary-coded instructions from memory
Decodes the instructions into a series of simple actions
Carries out these actions in a sequence of steps

## Slide 10: Input / Output
They are used to take data from outside world or send data to the outside world
I/O devices are connected with microprocessor through I/O ports
Example: Keyboards, video display terminals, printers, modems

## Slide 13: Memory
It stores the binary codes for the sequences of instructions
It stores binary coded data
Example: ROM, RAM, magnetic / optical disks

## Slide 14: Memory Organization:
Processor memory
Primary or main memory
Secondary memory

## Slide 15: Processor Memory:
It refers to the microprocessor registers which are used to hold temporary results when computation is in progress
No speed disparity between these registers and microprocessor because they are fabricated using the same technology
Costly

## Slide 16: Primary Memory
This is the storage area in which all programs are executed
The microprocessor can directly access only those items that are stored in primary memory
All programs and data must be within the primary memory prior to execution
Example: ROM, RAM

## Slide 17: Secondary Memory
It stores program and data in excess of main memory
Microprocessor can not directly execute programs which are stored in secondary memory
In order to execute these programs, the microprocessor must transfer them to its main memory by a system program called operating system
Example: Floppy disk, Hard disk etc.

## Slide 18
Figure: ROM

## Slide 19
18
Figure: RAM

## Slide 20
19
Figure: Floppy Disk

## Slide 21
20
Figure: Hard Disk

## Slide 22: BUS
The bus is an electrical path that connects the CPU, memory, and the other hardware devices on the motherboard.
The bus is a group of parallel wires.
The number of wires in the bus affects the speed at which data can travel between hardware components, just as the number of lanes on a highway affects how long it takes people to reach their destinations.
Because each wire can transfer 1 bit of data at a time, an 8-wire bus can move 8 bits at a time, which is a full byte. A 16-bit bus can transfer 2 bytes, and a 32-bit bus can transfer 4 bytes at a time. Newer model computers have a 64-bit bus, which transfers 8 bytes at a time.

## Slide 23: Figure: BUS
With a wider bus, the computer can move more data in the same amount of time (or the same amount of data in less time).

## Slide 26: Address Bus
The address bus is a set of wires. It consists of 16, 20, 24, 32 or 36 parallel unidirectional signal lines
On these lines the CPU sends out the address of the memory location or I/O port that is to be written to or read from
The number of locations that the CPU can address is determined by the number of address lines

## Slide 27: Data Bus
The data bus is a set of wires which consists of 8, 16, 32 parallel bidirectional signal lines
Many devices in the system will have their output connected to data bus, but only one device at a time will have its output enabled

## Slide 28: Control Bus
The control bus is a set of wires which consists of 4 to 10 parallel signal lines
The CPU sends out signals on the control bus to enable the outputs of addressed memory devices or I/O devices
Example of control signals: Memory read, Memory write